## Slide 1: Haptic Training Simulators
Andrew Crossan and
Stephen Brewster
Glasgow Interactive Systems Group
Department of Computing Science
University of Glasgow
ac, stephen@dcs.gla.ac.uk
www.dcs.gla.ac.uk/~stephen
9-10/10/2000

## Slide 2: Overview
Introduction and background to technology
  Multi-3D demo
Haptic training simulators
Glasgow work
  Pulsing demo
  Palpation demo
Conclusions
Demos

## Slide 3: Haptics and Touch
Haptic (hap'tik) :
adj.[Gr. haptein, to touch + ic]
  of, or having to do with, the sense of touch
  Webster's New World Dictionary
Computer haptics is difficult to describe - should be experienced

## Slide 4: The Sense of Touch
Relatively unused in computing
Beginning to change - devices are emerging
Unique feature
  Fully duplex channel. You can both transmit and receive information simultaneously
Touch is a complex sense consisting of several distinct sensory channels

## Slide 5: Terminology
Haptic
  Relating to the sense of touch
  Most general term
Kinesthetic
  The feeling of motion. Relating to sensations originating in muscles, tendons and joints

## Slide 6: Terminology
Tactile
  Pertaining to the cutaneous sense - the sensation of pressure (temperature and pain)
Force feedback
  Relating to the mechanical production of information sensed by the kinesthetic system

## Slide 7: Tactile Technologies
Tactile information is produced chiefly by perturbing the skin
Pins - as in devices for Braille display
Air jets - blow to produce a disturbance
Cushions of air - inflated or deflated to vary pressure on skin

## Slide 8: Tactile Technologies
Electrical stimulation - low levels of current provide a localised tingling sensation
  Typically used in gloves, or for larger body areas
These technologies all share the same lack of realism

## Slide 9: Force-Feedback Technologies 1
Kinesthetic information is produced by exerting mechanical forces
Technologies are easier to produce than tactile and are now reaching the home
Consoles - Dual Shock, Rumble Pack - cost £15

## Slide 10: Force-Feedback Technologies 2
PCs - 2 degree of freedom force-feedback joysticks cost £80
Force-feedback mice - 3 degree of freedom mice are now available costing £100

## Slide 11: Force-Feedback Technologies 3
The PHANToM is a state-of-the-art research device
Provides 6 dof in, 3 dof out
Costs >£25,000

## Slide 12: Example: Multi 3D

## Slide 13: The PHANToM
Originally developed for VR environments
Produces rich range of feedback suitable for many of applications
Visual models created in OpenGL or VRML
Set object haptic properties
  Stiffness
  Dynamic/static friction
  Damping

## Slide 14: Why Haptic Training Simulators for A&E?
Safe, controllable environment
Objective performance rating
Cost
Increased access
Flexibility
  Simulate a wide range of cases/complications/diseases
  Combination with anatomical and physiological models

## Slide 15: Performance Feedback
Important for learning
Complex multi-dimensional task
  the outcome is more than just success or failure
Results usually presented post-procedure
  Dependent on simulator type (ie. MIS, Surgery, Palpation…)
  Tissue damage/time taken/correct diagnosis etc.
  Can chart performance over time
Objective performance rating
  Useful for assessment/certification

## Slide 16: Medical Haptics 1
MIS Simulators - (KISMET, MIST-VR)

## Slide 17: Medical Haptics 2
Surgery Simulators (Penn State Suture Simulation, Cathsim)

## Slide 18: Medical Haptics 3
Palpation Simulators (Rutgers Prostate Simulator, Glasgow HOPS)

## Slide 19: Glasgow Work
Collaboration with Glasgow University Vet School and Weipers Equine Centre
Produce a training simulation environment
  Horse Ovary Palpation Simulation (HOPS)
  Pulsing simulator

## Slide 20: Pulsing Demo

## Slide 21: HOPS
Horse Ovary Palpation
  Internal examination
  Diagnosis through haptic properties only
  Limited access for students
Preliminary study has been carried out
  As good as traditional methods...
  But room for improvement

## Slide 22: HOPS Demo

## Slide 23: Multimodal Cues
Cues Haptic/Auditory/Graphic
Presented during the procedure
Used to provide performance feedback or guidance through the Virtual Environment
Can present different levels of help depending on the students experience

## Slide 24: Current Work Extending HOPS
Incorporating feedback cues
Improvements to the models
  Different force models
  Dual PHANToM palpation - An initial haptic object identification pilot has been run using HOPS

## Slide 25: Limitations
Fidelity
Immaturity of technology
  PHANToM allows only a single point of contact
  Two finger maximum, not whole hand with high fidelity
  Devices tend to be tactile or kinesthetic, not both
Validation of simulators

## Slide 26: Conclusions
Haptics has great potential for training simulators
Preliminary studies suggest haptics can be a useful training tool
Potential benefits to A&E
  Training without risk to patients
  Training for rare cases

## Slide 27: Haptic Training Simulators
Andrew Crossan and
Stephen Brewster
Glasgow Interactive Systems Group
Department of Computing Science
University of Glasgow
ac, stephen@dcs.gla.ac.uk
www.dcs.gla.ac.uk/~stephen
9-10/10/2000